## Slide 1: Centre for Research in Art of Film and Television
B-11, IMM BUILDING. QUTAB INSTITUTIONAL AREA,
NEW DELHI-110016
Tel: 98 99 25 11 33 / 44 / 55
www.craftfilmschool.com

## Slide 2: Film Sound
Signal Processors

## Slide 3: Signal Processing
Signal processing is concerned with the electronic manipulation of audio signals.
Analog processors operate directly on the electrical signal, while digital processors operate mathematically on the digital representation of that signal.

## Slide 4: Ways of Processing
Analog: The Audio Signal in the form of Electrical voltage or Current is physically altered. Analog is the continuous mathematical representation of Sound pressure levels to Voltage/Current
Digital: A digital representation expresses the audio waveform as a sequence of symbols, usually binary numbers. This permits signal processing using digital circuits such as digital signal processors, microprocessors and general-purpose computers.
Most modern audio systems use a digital approach as the techniques of digital signal processing and are much more powerful and efficient than analog domain signal processing.

## Slide 5: How is Signal Processed?
Equalizer
Compressor
Limiter
Gate
Chorus
Phaser
Flanger
Reverb
Delay
Echo

## Slide 6: Equalizer
Different frequency bands are attenuated or boosted to produce desired spectral characteristics. Moderate use of equalization ("EQ") can be used to "fine-tune" the tonal quality of a recording; extreme use of equalization, such as heavily cutting a certain frequency can create more unusual effects.

## Slide 7: Equaliser
Filtering - Equalization is a form of filtering. In the general sense, frequency ranges can be emphasized or attenuated using low-pass, high-pass, band-pass or band-stop filters. Band-pass filtering of voice can simulate the effect of a telephone because telephones use band-pass filters

## Slide 8: Compressor
The reduction of the dynamic difference in a sound to avoid unintentional fluctuation in the dynamics.
Dynamics is ”How loud” or “How Soft”

## Slide 9: Limiter
Process by which the amplitude of a signal is prevented from exceeding a predetermined value(also called Threshold)

## Slide 10: Gate
A Gate Allows the Signal Above the threshold to Pass and Reject all Signal Below

## Slide 11: Chorus
A delayed signal is added to the original signal with a constant delay. The delay has to be short in order not to be perceived as echo, but above 5 ms to be audible. If the delay is too short, it will destructively interfere with the un-delayed signal and create a flanging effect. Often, the delayed signals will be slightly pitch shifted to more realistically convey the effect of multiple voices.

## Slide 12: Phaser
Another way of creating an unusual sound: the signal is split, a portion is filtered with an all-pass filter to produce a phase-shift, and then the unfiltered and filtered signals are mixed. The phaser effect was originally a simpler implementation of the flanger effect since delays were difficult to implement with analog equipment. Phasers are often used to give a "synthesized" or electronic effect to natural sounds, such as human speech.

## Slide 13: Flanger
A delayed signal is added to the original signal with a continuously variable delay (usually smaller than 10 ms). This effect is now done electronically using DSP, but originally the effect was created by playing the same recording on two synchronized tape players, and then mixing the signals together. As long as the machines were synchronized, the mix would sound more-or-less normal, but if the operator placed his finger on the flange of one of the players (hence "flanger"), that machine would slow down and its signal would fall out-of-phase with its partner, producing a phasing effect. Once the operator took his finger off, the player would speed up until its tachometer was back in phase with the master, and as this happened, the phasing effect would appear to slide up the frequency spectrum. This phasing up-and-down the register can be performed rhythmically.

## Slide 14: Reverb
A reverb, is created when a sound or signal is reflected causing a large number of reflections to build up and then decay as the sound is absorbed by the surfaces of objects in the space – which could include furniture, people, and air. This is most noticeable when the sound source stops but the reflections continue, decreasing in amplitude
Reverberation is frequency dependent: the length of the decay, or reverberation time, receives special consideration in the architectural design of spaces which need to have specific reverberation times to achieve optimum performance for their intended activity.

## Slide 15: Delay
Delay is an audio effect and an effects unit which records an input signal to an audio storage medium, and then plays it back after a period of time.
Delay effects range from a subtle echo effect to a pronounced blending of previous sounds with new sounds.

## Slide 16: Echo
Echo is a reflection of sound that arrives at the listener with a delay after the direct sound. The delay is directly proportional to the distance of the reflecting surface from the source and the listener. Typical examples are the echo produced by the bottom of a well, by a building, or by the walls of an enclosed room and an empty room.
A true echo is a single reflection of the sound source.

## Slide 17: Audio Effects
Distortion
Overdrive
Pitch Shift
Time Stretch
Resonators
Robotic Voice Effects
Distortion is the alteration of the waveform of an information-bearing signal, such as an audio signal representing sound
Distortion is usually unwanted, and so engineers strive to eliminate or minimize it. In some situations, however, distortion may be desirable.
Eg: In FM broadcasting and noise reduction systems like the Dolby noise reduction system, an audio signal is deliberately distorted in ways that emphasize aspects of the signal that are subject to electrical noise, then it is symmetrically "undistorted" after passing through a noisy communication channel, reducing the noise in the signal. Distortion is also used as a musical effect, particularly with electric guitars.

## Slide 18: Over Drive
Overdrive is the form of audio signal processing used to alter the sound of amplified electric musical instruments, usually by increasing their gain, producing a "fuzzy", "growling", or "gritty" tone.

## Slide 19: Pitch Shift
Pitch shifting is a sound technique in which the original pitch of a sound is raised or lowered. Effects units that raise or lower pitch by a pre-designated musical interval (transposition) are called pitch shifters or pitch benders.
A harmonizer is a type of pitch shifter that combines the "shifted" pitch with the original pitch to create a two or more note harmony.
Pitch scaling is the process of changing the pitch without affecting the speed.

## Slide 20: Time Stretch
Time stretching is the process of changing the speed or duration of an audio signal without affecting its pitch.

## Slide 21: Resonators
Emphasize harmonic frequency content on specified frequencies. These may be created from parametric EQs or from delay-based comb-filters.
A resonator is a device or system that exhibits resonance or resonant behavior, ie it naturally oscillates at some frequencies, called its resonant frequencies, with greater amplitud than at others. The oscillations in a resonator can be either electromagnetic or mechanical (including acoustic). Resonators are used to either generate waves of specific frequencies or to select specific frequencies from a signal.

## Slide 22: Robotic Voice Effects
The vocoder was originally designed to aid in the transmission of voices over telephony systems. In musical applications the original sounds, either from vocals or from other sources such as instruments, are used and fed into a system of filters and noise generators. The input is fed through band-pass filters to separate the tonal characteristics which then trigger noise generators. The sounds generated are mixed back with some of the original sound and this gives the effect.