## Slide 1: Audio Post-Production
Art of Mixing
Mixing Consoles & Audio Equipment

## Slide 2: Post-production
Post-production is part of the process of filmmaking, video production, and photography. Post-production includes all stages of production occurring after shooting or recording individual program segments.

## Slide 3: Processes
Post-production is many different processes grouped under one name. These typically include:
Video editing the picture of a television program using an edit decision list (EDL)
Writing, (re)recording, and editing the soundtrack.
Adding visual special effects - mainly computer-generated imagery (CGI) and digital copy from which release prints will be made (although this may be made obsolete by digital-cinema technologies).
Sound design, sound effects, ADR, foley, and music, culminating in a process known as sound re-recording or mixing with professional audio equipment.
Transfer of color motion picture film to video or DPX with a telecine and color grading (correction) in a color suite.
The post-production phase of creating a film usually takes longer than the actual shooting of the film and can take several months to complete because it includes the complete editing, color correction, and the addition of music and sound. The process of editing a movie is also seen as the second directing because through post-production it is possible to change the intention of the movie. Furthermore, through the use of color grading tools and the addition of music and sound, the atmosphere of the movie can be heavily influenced. For instance, a blue-tinted movie is associated with a cold atmosphere and the choice of music and sound increases the effect of the shown scenes to the audience.
Post-production was named a "dying industry" by Phil Izzo. The once exclusive service offered by high-end post-production facilities have been eroded away by video editing software that operates on a non-linear editing system (NLE). As such, traditional (analogue) post-production services are being surpassed by digital, leading to sales of over $6 billion annually.

## Slide 4: Television
In television, the phases of post-production include: video editing, sound editing, animation and visual effects insertions, viewing and the start of the airing process.

## Slide 5: Music
Techniques used in music post-production include comping (compiling the best portions of multiple takes into one superior take), timing and pitch correction (perhaps through beat quantization), and adding effects. This process is typically referred to as mixing and can also involve equalization and adjusting the levels of each individual track to provide an optimal sound experience. Contrary to the name, post-production may occur at any point during recording and production process and is non-linear and nonveridic.

## Slide 6: Recording
Before the introduction of multitrack recording, all sounds and effects that were to be part of a record were mixed at one time during a live performance. If the recorded mix wasn't satisfactory, or if one musician made a mistake, the selection had to be performed over until the desired balance and performance was obtained. With the introduction of multi-track recording, the production of a modern recording changed into one that generally involves three stages:
Recording
Overdubbing
Mixing

## Slide 7: OverDubbing
Overdubbing (the process of making an overdub, or overdubs) is a technique used in audio recording, whereby a musical passage is recorded two or more times. This practice can be found with singers, as well as with instruments, or ensembles/orchestras.
In vocal performances the performer usually listens to an existing recorded performance (usually through headphones in a recording studio) and simultaneously plays a new performance along with it, which is also recorded. The intention is that the final mix will contain a combination of these "dubs".
Another kind of overdubbing is 'Tracking' (or "laying the basic tracks"), where tracks containing the rhythm section (usually including drums) is recorded first, then following up with overdubs (solo instruments, such as keyboards or guitar, then finally vocals). This method has been the standard technique for recording popular music since the early 1960s. Today, overdubbing can be accomplished even on basic recording equipment, or a typical PC equipped with a sound card, using digital audio workstation software

## Slide 8: Audio Mixing
Audio mixing is the process by which multiple sounds are combined into one or more channels (Mono, Stereo & Surround). In the process, a source's volume level, frequency content, dynamics, and panoramic position are manipulated and or enhanced. The tracks that are blended together by using various processes such as equalization. Compression etc. This practical, aesthetic, or otherwise creative treatment is done in order to produce a finished version that is appealing to listeners.
Audio mixing techniques and approaches can vary widely, and due to the skill-level or intent of the mixer, can greatly affect the qualities of the sound recording.
Audio mixing is practiced for music, film, television and live sound. The process is generally carried out by a mixing engineer operating a mixing console or digital audio workstation.
Audio mixing techniques largely depend on music genres and the quality of sound recordings involved. The process is generally carried out by a mixing engineer, though sometimes the record producer or recording artist may assist. After mixing, a mastering engineer prepares the final product for production.

## Slide 9: Audio Mix for Film & Television
Audio mixing for film and television is a process during the post-production stage of a moving image program by which a multitude of recorded sounds are combined. In the process, the source's signal level, frequency content, dynamics and panoramic position are commonly manipulated and effects added.
The process takes place on a mix stage, typically in a studio or theater, once the picture elements are edited into a “FINAL Version”. Normally the engineer will mix four main audio elements: speech (dialogue, ADR, voice-overs, etc.), ambience (or atmosphere), sound effects, and music.

## Slide 10: Mixing Consoles
A mixer (mixing console, mixing desk, mixing board, or software mixer) is the operational heart of the mixing process. Mixers offer a multitude of inputs, each fed by a track from a multitrack recorder. Mixers typically have 2 main outputs (in the case of two-channel stereo mixing) or 8 (in the case of surround).

## Slide 11: Mixing Consoles
Mixers offer three main functionalities.
Summing signals together, which is normally done by a dedicated summing amplifier or, in the case of a digital mixer, by a simple algorithm.
Routing of source signals to internal buses or external processing units and effects.
On-board processors with equalizers and compressors.

## Slide 12: Digital Audio Workstations
Digital audio workstations (DAW) can perform many mixing features in addition to other processing. An audio control surface gives a DAW the same user interface as a mixing console. The distinction between a large console and a DAW equipped with a control surface is that a digital console will typically consist of dedicated digital signal processors for each channel. DAWs can dynamically assign resources like digital audio signal processing power, but may run out if too many signal processes are in simultaneous use. This overload can often be solved by increasing the capacity of the DAW.

## Slide 13: Outboard gear and plugins
Outboard gear (analog) and software plugins (digital) can be inserted into the signal path to extend processing possibilities. Outboard gear and plugins fall into two main categories:
Processors – these devices are normally connected in series to the signal path, so the input signal is replaced with the processed signal. Examples include equalization, dynamic processing (compressors, gates, expanders, and limiters). However, some processors are also used in parallel, as is the case in techniques such as parallel compression/limiting (a.k.a. New York compression) and sidechain equalization.
Effects – these can be considered as any unit that has an effect upon the signal, the term is mostly used to describe units that are connected in parallel to the signal path, and therefore they add to the existing sounds but do not replace them. Examples of common effects include reverb and delay. Some effects are more commonly used in series like chorus, flange, and vibrato.

## Slide 14: Processes that affect levels
Faders – used to attenuate or boost the level of signals.
Pan pots – A fundamental part of configuration in recording console is panning. Pan pots are devices that place sound among the channels: L, C, R, LS, and RS. They are also used to pan signals to the left or right and in surround, to the back or front.
Compressors – A device which attenuates the volume of a track when its volume passes beyond a set threshold. The primary use of a compressor in mixing is to limit the dynamics of a track. Compressors are equipped with a number of controls including the threshold, the amount of compression etc
Expansion – The Expansion device does exactly the opposite of what the compressor does. It increases the volume range of a source and may do so across a wide dynamic range or may be restricted to a narrower region by control functions.
Limiters – A limiter is a compressor with a Ratio of 10:1 or higher. Often referred to as a "brick-wall" limiter, some limiters have extremely high (or infinite) Ratios meaning that little to no audio surpasses the threshold. Limiters are most commonly used in mixing to strictly limit the maximum output volume of a track, buss, or overall mix. Limiters are especially useful in digital mixing to avoid clipping.

## Slide 15: Processes that affect frequency response
Processes that primarily affect the frequency response of the signal are generally seen as second in importance to level control. These processes clean the audio signal, enhance interchangeability between other signals, adjust for the loudness effect, and generally create a much more pleasant or deliberately worse sound. There are two principle frequency response processes – equalization and filtering.
Equalizers – The simplest description of EQ is the process of altering the frequency response in a manner similar to what tone controls do on a stereo system. Professional EQs dissect the audio spectrum into three or four parts which may be called the low-bass, mid-bass, mid-treble, and high frequency controls.
Filters – Filters are used to eliminate certain frequencies from the output. Filters strip off the any part of the audio spectrum. There are various types of filters. A high-pass filter (low-cut) is used to remove excessive room noise at low frequencies. A low-pass filter (high-cut) is used to help isolate a low frequency instrument playing in a studio along with others. And a band-pass filter is a combination of high- and low-pass filters, also known as a telephone filter (because a sound lacking in high and low frequencies resembles the quality of sound transmitted and received by telephone).

## Slide 16: Processes that affect time
Reverbs – Reverbs are used to simulate boundary reflections created in a real room, adding a sense of space and depth to otherwise 'dry' recordings. Another use is to distinguish among auditory objects; all sound having one reverberant character will be categorized together by human hearing in a process called auditory streaming. This is an important feature in layering sound, in depth, from in front of the speaker to behind it.
Before the advent of electronic reverb and echo processing, physical means were used to generate the effects. An echo chamber, a large reverberant room, could be equipped with a speaker and at least two spaced microphones. Signals were then sent to the speaker and the reverberation generated in the room was picked up by the two microphones, constituting a "stereo return".

## Slide 17: Processes that affect space
Panning – Static panning is used to control the location of phantom sources. This is achieved by leveraging a panning law that calculates the perceived location from the balance of loudspeakers' signal volumes or their relative time shift. Source locations can be located at any location between a pair of frontal or rear loudspeakers. Dynamic panning alters the volume or time balance of the loudspeaker pair to create the impression of moving sources.
Pseudostereo – Pseudostereo techniques are applied to broaden the sound image. This way the apparent source width or the degree of listener envelopment is increased. A number of pseudostereo recording and mixing techniques are known from the viewpoint of audio engineers and researchers.

## Slide 18: Mixdown
The mixdown process converts a program with a multiple-channel configuration into a program with fewer channels. Common examples include downmixing from 5.1 surround sound to stereo, and stereo to mono. In the former case, the left and right surround channels are blended with the left and right front channels. The center channel is blended equally with the left and right channels. The LFE channel is either mixed with the front signals or not used. Because these are common scenarios, it is common practice to verify the sound of such downmixes during the production process to ensure stereo and mono compatibility.
The alternative channel configuration can be explicitly authored during the production process with multiple channel configurations provided for distribution. For example, a stereo mix can be put on DVDAudio discs or Super Audio CDs along with the surround mix. Alternatively, the program can be automatically downmixed by the end consumer's audio system. For example, a DVD player or sound card may downmix a surround sound program to stereophonic sound (two channels) for playback through two speakers.

## Slide 19: Mixing in Surround Sound
Any device having a number of multiple bus consoles (typically having eight or more buses) can be used to create a 5.1 surround sound mix, but this may be frustrating if the device is not designed to facilitate signal routing, panning and processing in a surround sound environment. Whether working in an analog hardware, digital hardware, or DAW "in-the-box" mixing environment, the ability to pan mono or stereo sources and place effects in the 5.1 soundscape and monitor multiple output formats without difficulty can make the difference between a successful or compromised mix. Mixing in surround is very similar to mixing in stereo except that there are more speakers, placed to "surround" the listener. In addition to the horizontal panoramic options available in stereo, mixing in surround lets the mix engineer pan sources within a much wider and more enveloping environment. In a surround mix, sounds can appear to originate from many more or almost any direction depending on the number of speakers used, their placement and how audio is processed.
There are two common ways to approach mixing in surround:
Expanded Stereo – With this approach, the mix will still sound very much like an ordinary stereo mix. Most of the sources such as the instruments of a band, the vocals, and so on, will still be panned between the left and right speakers, but lower levels might also be sent to the rear speakers in order to create a wider stereo image, while lead sources such as the main vocal might be sent to the center speaker. Additionally, reverb and delay effects will often be sent to the rear speakers to create a more realistic sense of being in a real acoustic space. In the case of mixing a live recording that was performed in front of an audience, signals recorded by microphones aimed at, or placed among the audience will also often be sent to the rear speakers to make the listener feel as if he or she is actually a part of the audience.
Complete Surround/All speakers are treated equally – Instead of following the traditional ways of mixing in stereo, this much more liberal approach lets the mix engineer do anything he or she wants. Instruments can appear to originate from anywhere, or even spin around the listener. When done appropriately and with taste, interesting sonic experiences can be achieved, as was the case with James Guthrie's 5.1 mix of Pink Floyd's The Dark Side of the Moon, albeit with input from the band. This is a much different mix from the 1970s quadrophonic mix.

## Slide 20: Mixing in Surround Sound
MSS – Multi Stereo Surround – This approach treats the speakers in a surround sound system as a multitude of stereo pairs. For example, a stereo recording of a piano, created using two microphones in an ORTF configuration, might have its left channel sent to the left rear speaker and its right channel sent to the center speaker. The piano might also be sent to a reverb having its left and right outputs sent to the left front speaker and right rear speaker, respectively. Additional elements of the song, such as an acoustic guitar recorded in stereo, might have its left and right channels sent to a different stereo pair such as the left front speaker and the right rear speaker with its reverb returning to yet another stereo pair, the left rear speaker and the center speaker. Thus, multiple clean stereo recordings surround the listener without the smearing comb-filtering effects that often occur when the same or similar sources are sent to multiple speakers.